## Slide 1: Graphics Hardware
CMSC 435/634

## Slide 2: A Graphics Pipeline
Transform
Shade
Clip
Project
Rasterize
Texture
Z-buffer
Interpolate
Vertex
Fragment
Triangle

## Slide 3: Computation and Bandwidth
67 GFLOPS
1.1 TFLOPS
75 GB/s
13 GB/s
335 GB/s Texture
45 GB/s Fragment
Vertex
Triangle
Fragment
Based on:
• 100 Mtri/sec (1.6M/frame@60Hz)
• 256 Bytes vertex data
• 128 Bytes interpolated
• 68 Bytes fragment output
• 5x depth complexity
• 16 4-Byte textures
• 223 ops/vert
• 1664 ops/frag
• No caching
• No compression

## Slide 4: Data Parallel
Task
Task
Task
Task
Distribute
Merge

## Slide 5: Sort First
Vertex
Distribute objects by screen tile
Triangle
Fragment
Some pixels
Some objects
Vertex
Triangle
Fragment
Vertex
Triangle
Fragment
Objects
Screen

## Slide 6: Sort Middle
Vertex
Distribute objects or vertices
Merge & Redistribute by screen location
Vertex
Vertex
Triangle
Fragment
Triangle
Fragment
Triangle
Fragment
Triangle
Fragment
Some pixels
Some objects
Some objects
Objects
Screen

## Slide 7: Screen Subdivision
Tiled
Interleaved

## Slide 8: Sort Last
Vertex
Triangle
Fragment
Distribute by object
Z-merge
Vertex
Triangle
Fragment
Vertex
Triangle
Fragment
Full Screen
Some objects
Objects
Screen

## Slide 9: Graphics Processing Unit (GPU)
Sort Middle(ish)
Fixed-Function HW for clip/cull, raster, texturing, Ztest
Programmable stages
Commands in, pixels out

## Slide 10: GPU Computation
Vertex
Pixel
Triangle
Pipeline
…
Parallel
More Parallel
More Pipeline
More Parallel

## Slide 11: Architecture: Latency
CPU: Make one thread go very fast
Avoid the stalls
  Branch prediction
  Out-of-order execution
  Memory prefetch
  Big caches
GPU: Make 1000 threads go very fast
Hide the stalls
  HW thread scheduler
  Swap threads to hide stalls

## Slide 12: Architecture (MIMD vs SIMD)
CTRL
ALU
ALU
CTRL
ALU
ALU
CTRL
CTRL
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
MIMD(CPU-Like)
SIMD (GPU-Like)
CTRL
Flexibility
Horsepower
Ease of Use

## Slide 13: SIMD Branching
if( x ) // mask threads
// issue instructions
else // invert mask
// issue instructions
// unmask
Threads agree, issue if
Threads disagree, issue if AND else
Threads agree, issue else

## Slide 14: SIMD Looping
while(x) // update mask
// do stuff
They all run ‘till the last one’s done….
Useful
Useless

## Slide 15: GPU graphics processing model
Z-Buffer
Rasterize
Vertex
Geometry
Fragment
CPU
Displayed
Pixels
Texture/Buffer

## Slide 16: NVIDIA GeForce 6
[Kilgaraff and Fernando, GPU Gems 2]
Vertex
Rasterize
Fragment
Z-Buffer
Displayed
Pixels

## Slide 17: GPU graphics processing model
Z-Buffer
Rasterize
Vertex
Geometry
Fragment
CPU
Displayed
Pixels
Texture/Buffer

## Slide 18: GPU graphics processing model
CPU
Displayed
Pixels
Vertex
Geometry
Fragment
Rasterize
Z-Buffer
Texture/Buffer

## Slide 19: AMD/ATI R600 Dispatch

## Slide 20: SIMD Units
2x2 Quads (4 per SIMD)
20 ALU/Quad (5 per thread)
“Wavefront” of 64 Threads, executed over 8 clocks
2 Waves interleaved
Interleaving + multi-cycling hides ALU latency.
Wavefront switching hides memory latency.
GPR Usage determines wavefront count.
General Purpose Registers
4x32bit
(THOUSANDS of them)

## Slide 21: AMD/ATI R600
[Tom’s Hardware]

## Slide 22: NVIDIA Maxwell
[NVIDIA, NVIDIA GeForce GTX 980 Whitepaper, 2014]

## Slide 23: Maxwell SIMD Processing Block
32 Cores
8 Special Function
NVIDIA Terminology:
  Warp = interleaved threads
    Want at least 4-8
  Thread Block = Warps*Cores
Flexible Registers
  Trade registers for warps

## Slide 24: Maxwell Streaming Multiprocessor (SMM)
4 SIMD blocks
Share L1 Caches
Share memory
Share tessellation HW

## Slide 25: Maxwell Graphics Processing Cluster (GPC)
4 SMM
Share raster

## Slide 26: Full NVIDIA Maxwell
4 GPC
Share L2
Share dispatch

## Slide 27: NVIDIA Maxwell Stats
16 SM * 4 SIMD Blocks* 32 cores (2048 total)
4.6 TFLOPS, 144 Gtex/s, 224 MB/s
2MB L2 Cache
Compress between Memory and L2
  Saves 25%

## Slide 28: GPU Performance Tips

## Slide 29: Graphics System Architecture
Your Code
API
Driver
Current Frame
(Buffering Commands)
Previous Frame(s)
(Submitted, Pending Execution)
GPU
Produce
Consume
GPU
GPU(s)
Display

## Slide 30: GPU Performance Tips
API and Driver
  Reading Results Derails the train…..
    Occlusion Queries  Death
      When used poorly ….
    Framebuffer reads  DEATH!!!
      Almost always…
  CPU-GPU communication should be one way
    If you must read, do it a few frames later…

## Slide 31: GPU Performance Tips
API and Driver
  Minimize shader/texture/constant changes
  Minimize Draw calls
  Minimize CPUGPU traffic
    glBegin()/glEnd() are EVIL!
    Use static vertex/index buffers if you can
    Use dynamic buffers if you must
      With discarding locks…

## Slide 32: GPU Performance Tips
Shaders, Generally
  NO unnecessary work!
    Precompute constant expressions
    Div by constant  Mul by reciprocal
  Minimize fetches
    Prefer compute (generally)
    If ALU/TEX < 4+, ALU is under-utilized
    If combining static textures, bake it all down…

## Slide 33: GPU Performance Tips
Shaders, Generally
  Careful with flow control
    Avoid divergence
    Flatten small branches
    Prefer simple control structure
  Double-check the compiler
    Shader compilers are getting better…
  Look over artists’shoulders
    Material editors give them lots of rope….

## Slide 34: GPU Performance Tips
Vertex Processing
  Use the right data format
    Cache-optimized index buffer
    Small, 16-byte aligned vertices
  Cull invisible geometry
    Coarse-grained (few thousand triangles) is enough
    “Heavy” Geometry load is ~2MTris and rising

## Slide 35: GPU Performance Tips
Pixel Processing
  Small triangles hurt performance
    2x2 pixel quads  Waste at edge pixels
  Respect the texture cache
    Adjacent pixels should touch adjacent texels
    Use the smallest possible texture format
  Avoid dependent texture reads
  Do work per vertex
    There’s usually less of those (see small triangles)

## Slide 36: GPU Performance Tips
Pixel Processing
  HW is very good at Z culling
    Early Z, Hierarchical Z
  If possible, submit geometry front to back
  “Z Priming” is commonplace
    Render with simple shader to z-buffer
    Then render with real shader

## Slide 37: GPU Performance Tips
Blending/Backend
  Turn off what you don’t need
    Alpha blending
    Color/Z writes
  Minimize redundant passes
    Multiple lights/textures in one pass
  Use the smallest possible pixel format
  Consider clip/discard in transparent regions