## Slide 1: CMSC 611
Evaluating Cost
Some material adapted from Mohamed Younis, UMBC CMSC 611 Spr 2003 course slides
Some material adapted from David Culler, UC Berkeley CS252, Spr 2002 course slides, © 2002 UC Berkeley
Some material adapted from Hennessy & Patterson / © 2003 Elsevier Science

## Slide 2: Integrated Circuits
Silicon is a semiconductor
  Found in sand
  Does not conduct electricity well
Chemical processes can transform tiny areas of silicon to either:
  Excellent conductors (like copper)
  Excellent insulator (like glass)
  Areas that can conduct or insulate (a switch)
A transistor is simply an on/off switch controlled by electricity
Integrated circuits combine thousands to millions of transistors in a chip

## Slide 3: Microelectronics Process
Slices
20-30 processing steps
Dice
Package
Package Test
Die Test
Ship
Silicon ingots:
  6-12 inches in diameter and about 12-24 inches long
Impurities in the wafer can lead to defective devices and reduces the yield

## Slide 4: Integrated Circuits Costs
Die cost roughly goes with die area4

## Slide 5: What Affects Cost?
Learning curve:
  The more experience in manufacturing a component, the better the yield
  In general, a chip, board or system with twice the yield will have half the cost.
  The learning curve is different for different components, complicating design decisions
Volume
  Larger volume increases rate of learning curve
  Doubling the volume typically reduce cost by 10%
Commodities
  Are essentially identical products sold by multiple vendors in large volumes
  Foil the competition and drive the efficiency higher and thus the cost down

## Slide 6: Real World Examples
  From "Estimating IC Manufacturing Costs,” by Linley Gwennap, Microprocessor Report, August 2, 1993, p. 15

## Slide 7: Cost vs. Price
Component Cost
Direct Cost
Gross Margin
Average Discount
Avg. Selling Price
List Price
15% to 33%
6% to 8%
34% to 39%
25% to 40%
Component Costs: raw material cost for the system’s building blocks
Direct Costs (add 18% to 53%) recurring costs: labor, purchasing, scrap, warranty
Gross Margin (add 82% to 186%) nonrecurring costs: R&D, marketing, sales, equipment maintenance, rental, financing cost, pretax profits, taxes
Average Discount to get List Price (add 33% to 73%): volume discounts and/or retailer markup

## Slide 8: Example: Price vs. Cost
Chip Prices (August 1993) for a volume of 10,000 units