## Slide 1: CMSC 611: Advanced Computer Architecture
Cache
Some material adapted from Mohamed Younis, UMBC CMSC 611 Spr 2003 course slides
Some material adapted from Hennessy & Patterson / © 2003 Elsevier Science

## Slide 2: Memory Hierarchy
Control
Datapath
Secondary
Storage
(Disk)
Processor
Registers
Main
Memory
(DRAM)
Second
Level
Cache
(SRAM)
On-Chip
Cache
Fastest
Slowest
Smallest
Biggest
Highest
Lowest
Speed:
Size:
Cost:
Compiler
Hardware
Operating System
Temporal Locality (Locality in Time):
   Keep most recently accessed data items closer to the processor
Spatial Locality (Locality in Space):
   Move blocks consists of contiguous words to the faster levels

## Slide 3: The Basics of Cache
Requesting Xn generates a miss and the word Xn will be brought from main memory to cache
Issues:
How do we know that a data item is in cache?
If so, How to find it?
Cache: level of hierarchy closest to processor
Caches first appeared in research machines in early 1960s
In every general-purpose computer produced today

## Slide 4: Memory Hierarchy Terminology
Slower Level
Memory
Faster Level
Memory
To Processor
From Processor
Block X
Block Y
Hit: data appears in some block in the faster level (example: Block X)
  Hit Rate: the fraction of memory access found in the faster level
  Hit Time: Time to access the faster level which consists of
    Memory access time + Time to determine hit/miss
Miss: data needs to be retrieve from a block in the slower level (Block Y)
  Miss Rate = 1 - (Hit Rate)
  Miss Penalty: Time to replace a block in the upper level + Time to deliver the block the processor
Hit Time << Miss Penalty

## Slide 5: Memory Hierarchy Design Issues
Block placement
  Where can a block be placed in the upper (faster) level?
Block identification
  How is a block found if it is in the upper (faster) level?
Block replacement
  Which block should be replaced on a miss?
Write strategy
  What happens on a write?

## Slide 6: Block Placement: Direct Mapped
Cache is a table of blocks
Every block in memory maps to one and only one block in cache
Many memory blocks map to the same cache block

## Slide 7: Block Placement: Set Associative
Cache is a table of N blocks each
  Set of N blocks at each index
  N-way associative
Every block in memory maps to one and only one index, but can use any of the N blocks at that index
To keep size the same, divide number of indices by N

## Slide 8: Block Placement: Fully Associative
Any block in memory can use any block in the cache
Like set associative where number of indices = 1 and associativity N = full cache size.

## Slide 9: Block Identification
Partition address
Offset within block
  000000b for first byte in block
  111111b for last byte in block
Index
  Which line in the cache?
Tag
  Rest of the address
  Store in cache to know you have the right block
Tag
Index
Offset

## Slide 10: Block Identification

## Slide 11: Block Replacment
If all blocks at index are already in use
  Must replace one. Which one?
Only one choice for Direct Mapped
Associative:
  Least Recently Used (LRU)
  Random

## Slide 12: Write Strategy
Write Back
  Write block to lower level when evicted from upper-level cache
Write Through
  Update upper-level cache and forward write to lower-level for each write